## Slide 1
Propagation Mechanism
Fig: Multipath Signal at Outdoor
Reflection from mountains
Reflection from tall building
Diffraction
Direct ray

## Slide 2
Propagation Mechanism
Reflection
Reflection occurs when the Electromagnetic waves impinge on objects which are much greater than the wavelength of the traveling wave.
Reflection from Dielectrics
Ɛ – Permittivity
σ- Conductance
μ- Permeability
Courtesy to Theodore S. Rappaport
©2002, 1996 Prentice Hall PTR

## Slide 3
Propagation Mechanism
Brewster angle: Brewster's angle (also known as the polarization angle) is an angle of incidence at which wave is perfectly transmitted through surface, with no reflection.
Sin (θB)= (ε1 / (ε1 + ε2 )) 1/2
First medium is free space:
sin (θB)= (εr-1)1/2/(εr2-1)1/2
Reflection from perfect conductors
- EM energy cannot pass through perfect conductor
- All of its energy is reflected
Occurs only for Vertical polarization

## Slide 4
Example
Calculate the Brewster angle for a wave impinging on the ground with a permittivity of 7. Assume the frequency to 200MHz.
Solution: sin (θB)= (εr-1)1/2/(εr2-1)1/2

## Slide 5
Propagation Mechanism
Scattering
  This occurs when the size of the objects is less than the wavelength of the travelling wave.
  Occurs when a radio wave impinges on a rough surface, the reflected energy is spread out in all directions.
Surface roughness is tested using Critical height hc of surface perturbance for a given angle of incidence θi.
hc= λ/8 sin θi.
A surface is considered smooth if h <hc and rough if h>hc.

## Slide 6
Propagation Mechanism
Diffraction:
Occurs when the radio path between the transmitter and the receiver is obstructed by a surface that has sharp irregularities.
It results in bending of the waves around the object.
Reflection from mountains
Reflection from tall building
Diffraction from roof
Direct ray

## Slide 7
Mobile Radio Propagation
At VLF, LF, MF bands, radio waves follow the ground.
Area between the surface of the earth and the ionosphere for transmission.
Ground wave radio signal propagation is ideal for relatively short distance propagation as the wave front of the ground wave travels along the Earth's surface it is attenuated.
Frequency of the radio signal is one of the major determining factor as losses rise with increasing frequency.
The type of antenna and its polarization has a major effect on ground wave propagation. Vertical polarization is subject to considerably less attenuation than horizontally polarized signals.
Earth
Atmosphere
Home
Radio Tower
Ground Wave Propagation

## Slide 8
Ionospheric Propagation
HF Bands
D layer- Lowest layer existing at an average height of 70Km.It reflects VLF , LF.
E layer- Exists at an average height of 100km. It reflects MF waves.
F1 and F2 layer- Exists at a average height of 180 Km. Reflects HF waves.
Earth Surface
Sky wave propagation
Ionospheric Layers
D
E
F2
F1

## Slide 9
Space Wave Propagation
The radio waves having high frequencies are basically called as space waves.
Occur within the lower 20 km of the atmosphere (troposphere), and are comprised of a direct and reflected wave(Tropospherical Propagation).
Space waves can travel directly or can travel after reflecting from earth’s surface to the troposphere surface of earth.
Frequency Bands VHF, UHF, SHF, EHF use space wave propagation.
Earth Surface
Transmitter
Receiver
Direct wave
Reflected wave

## Slide 10
Space wave Propagation
Limitations of space wave propagation
Space waves are limited to the curvature of the earth.
These waves have line of sight propagation, means their propagation is along the line of sight distance.
Increase the transmission distance can be done by simply extending the heights of both the sender as well as the receiver antenna.
This type of propagation is used basically in radar and television communication.
Directional antennas are used for space wave propagation.

## Slide 11
Summary
The radio waves take multipath during the propagation
Radio waves get reflected, diffracted, scattered before reaching the receiver
Radio waves propagate through various modes of propagation like ground wave, Ionosphere propagation and Space wave propagation.