## Slide 1
Channel Assignment Strategies
For efficient utilization of the radio spectrum, a frequency reuse was adopted with the objectives of increasing capacity of the cellular system and minimizing interference .
Two approaches :
Fixed Channel assignment
Dynamic channel assignment

## Slide 2
Fixed Channel Assignment
Each cell is allocated a predetermined set of voice channels.
Any call attempt within the cell can only be served by the unused channels in that particular cell.
If all the channels in that cell are occupied, the call is blocked and the subscriber does not receive service.
Many Variations in the fixed channel assignment.
- Borrowing strategy
- Cells borrow channels from neighboring cells
- MSC supervise the borrowing activity
- Borrowing of a channel does not interfere with any of the calls in the donor
cell

## Slide 3
Dynamic Channel Assignment
Voice channels are not allocated to different cells permanently.
Each time a call request is made, the serving base station requests a channel from the MSC.
The switch then allocates a channel to the requested cell following an algorithm that takes into account the likelihood of fixture blocking within the cell, the frequency of use of the candidate channel, the reuse distance of the channel.
Advantage of increased channel utilization and decreased probability of blocked call.
MSC continuously collect the data on real time occupancy, traffic distribution , radio signal strength indications(RSSI)of all channels.
Disadvantage: Increases the computational load , storage on the MSC.
Courtesy to Theodore S. Rappaport
©2002, 1996 Prentice Hall PTR

## Slide 4
Handoff In a Cellular Network
Handoff is the transition for any given user of signal transmission from one base station to a geographically adjacent base station as the user moves around.
Handover, in which the source and the target are different cells (even if they are on the same cell site) is called inter-cell handover.
Source and target are one and the same cell- Intra-cell Handover
- Interference in the channel causes the change of channel with in the cell.

## Slide 5
Purpose of Handoff
In telecommunications there may be different reasons why a handover might be conducted:
When the user is moving away from the area covered by one cell and entering the area covered by another cell.
In non-CDMA networks when the channel used by the phone becomes interfered by another phone using the same channel in a different cell, the call is transferred to a different channel in the same cell or to a different channel in another cell in order to avoid the interference
In CDMA networks a handover may be induced in order to reduce the interference to a smaller neighboring cell .

## Slide 6
Summary
Channel assignment strategies involved two approaches namely fixed channel and dynamic channel assignment.
Variations in the fixed channel assignment strategy called borrowing strategy where the channel is borrowed from the neighboring cell.
Handoff is the transition for any given user of signal transmission from one base station to a geographically adjacent base station as the user moves around.
Purpose of handoff is induced in order to reduce the interference to a smaller neighboring cell .