## Slide 1: SPIN (Sensor Protocols for Information via Negotiation)
SPIN Focus on efficient dissemination of individual sensor observations to all the sensors in a ntk- treat all sensors as potential sink nodes
SPIN family of protocols incorporates two key innovations
  negotiation
  resource-adaptation
Implosion
Overlap
Resource Blindness
Notes: Each sensor node has its own resource manager that keeps track of resource consumption; applications probe the manager before transmitting or processing data.

## Slide 2: Resources for SPIN
Meta data – used to describe the message
Resource Manager – keeps track of energy
Notes: Sensors use meta-data to succinctly and completely describe the data that they collect. If x the meta-data descriptor
for sensor data x , then the size of X bytes must be shorter than the size of X , for SPIN to be beneficial. If two pieces of actual data are distinguishable, then their corresponding meta-data should be distinguishable

## Slide 3
A
B
D
E
C
F
G
ADV
REQ
DATA
ADV
Notes: When a SPIN-2 node observes that its energy is approaching a low-energy threshold, it adapts by reducing its participation in the protocol. In general, a node will only participate in a stage of the protocol if it believes that it can complete all the other stages of the protocol without going below the low-energy threshold. This conservative approach implies that, if a node receives some new data, it only initiates the threestage protocol if it believes it has enough energy to participate in the full protocol with all of its neighbors. Similarly if a node receives an advertisement, it does not send out a request if it does not have enough energy to transmit

## Slide 4: Directed Diffusion
Data generated by sensor nodes is named by attribute-value pair
Sink request data by sending interests for named data
Every node has an interest cache
Data matching the interest is drawn towards the sink
Intermediate nodes – may fuse data with their own or cache it
A sensing task is disseminated through the network as interests
Dissemination sets up gradients within the ntk designed to draw data

## Slide 5: Query & Response Format
Type four-legged animal
Interval 20ms
Duration 10s
Rect 100,100,200,400
Type four-legged animal
Instance elephant
Location 125,250
Confidence 0.85
Timestamp 01:20:40

## Slide 7
Type four-legged animal
Instance elephant
Location 125,250
Confidence 0.85
Timestamp 01:20:40 Data cache

## Slide 8
Type four-legged animal
Interval 10ms
Rect 100,100,200,400
Time stamp 01:22:35
Expiry 01:30:40

## Slide 9: Rumour Routing
A logical compromise between flooding queries and flooding event notifications
In the event that there is small data then data flooding may be better than event query flooding
Each node maintains – event table, neighbour table
Event may create an agent
Notes: Event broadcast or a query broadcast ? Query – if data large and no.of events are also large.
Agent – info on event – when a node receives an agent it updates the event table
Event table – distance and forwarding choice of event.

## Slide 10
vvv

## Slide 11
vvv

## Slide 12
vvv

## Slide 13
vvv

## Slide 14
vvv

## Slide 15
vvv

## Slide 16
vvv

## Slide 17
vvv

## Slide 18
vvv

## Slide 19
vvv

## Slide 20
vvv

## Slide 21
vvv
Notes: Query is sent in an random direction until it reaches the event.

## Slide 22
vvv
Notes: Query is sent in an random direction until it reaches the event.

## Slide 23
vvv
Notes: Query is sent in an random direction until it reaches the event.

## Slide 24
vvv
Notes: Query is sent in an random direction until it reaches the event.

## Slide 25
vvv
Notes: Query is sent in an random direction until it reaches the event.